Temp. Controlled Soldering Station

Features:

• This welding machine is an ideal welding tool for an

amateur, fancier, school, electronics plant and for

maintaining the service, producing with laboratory.

• It has the precise function of regulating temperature,

1 degree or 10 degrees per grade can be regulated

through the temperature regulating button, also can

control the temperature through 200°C, 300°C and

400°C button. There is a °C/°F convert button.

• When operation breakdown taken place, warnings will

appear through screen display and sound.

Specifications:

Power Supply Voltage : 110 Volt (110 to 130 Volt)/60Hz

230 Volt (220 to 240 Volt)/50Hz.

Electric Iron Power : 48 Watt.

Equipment Power Supply Fuse : T1 A/250 Volt (50 x 20mm Glass Pipe).

Regulating Scope of Temperature : 150° to 450°C.

Temperature Display : 2 x 31/2 Grades LCD Display

Display Scope : 150° to 450°C.

Display Precision : 5%.

Circumstance Humidity : +5°C to +40°C

Relative Humidity : <85% (Not in Humidification).

Atmospheric Pressure : 600 to 1000HPa.

Shell Size (W x H x D) : 210 x 125 x 135mm (Without Electric Iron).

Weight : About 1800 Grams.

Part Number Table

| Voltage Supply (V) | Part Number |
| --- | --- |
| 110 to 130 | D00675 |
| 220 to 240 | D00676 |