Digital Repair System

Soldering Station

Features:

• Especially designed for lead free soldering.

• Exceptional high-performance PTC in the desoldering iron

provide a long life and continuously controlled supply of

heat, suitable for desoldering all type of components and

easy removal of the residual solder.

• The temperature sensor on the top of the tips can check the

tip temperature quickly and decreasing the possibility of the

tip temperature falling off during the operating and suitable

for lead free soldering..

• The quick heat and strong power are for convenient and

clear soldering/desoldering all type of DIP components.

• Reasonable structure, single hand operation and strong

absorbing power can easily remove the residual solder from

the one-sided or two sided PCB.

Specifications:

Station:

Voltage Supply : 220 to 240V ac.

Power Consumption : 80W.

Vacuum Pressure : 600mm HG.

Desoldering Gun:

Power Consumption : 80W at 24V ac (Heat up Rating 130W).

Temperature : 160°C to 480°C.

Heating Element : Ceramic Heater.

Part Number Table

| Description | Part Number |
| --- | --- |
| Soldering Station | D00672 |